## Slide 1: Multi-Agent AI System for PETSc Simulation of Plasma in a Tokamak (for Nuclear Fusion Energy)
Presenter
Sarthak Sharma1,2
Intern and PhD student
1Division of Mathematics and Computer Science, Argonne National Laboratory,
2State University of New York at Buffalo.
ANL Learning Off The Lawn
Advisors
Dr Junchao Zhang1, Dr Lois Curfman McInnes1, Prof Matthew Knepley2.
July 29, 2026

## Slide 2: Contents
Why nuclear fusion energy needs trustworthy simulation
The modeling challenge
The problem: Grad–Shafranov equilibrium
The system: 3-layer multi-agent AI pipeline
The AI pipeline in action
AI-agent-generated PETSc solver (excerpt)
Verification: it is actually right
Decision-gate metrics
Fully autonomous: the built-in orchestrator
What we built and contributed
Takeaways and next steps

## Slide 3: Why nuclear fusion energy needs trustworthy simulation
Nuclear fusion could be a near-limitless clean energy source, if we can solve some challenges.
Combine light nuclei to create heavy nuclei (e.g., hydrogen isotopes converted to helium).
Small amount of mass converted to large amount of energy:
Source of energy in stars.
Deuterium–tritium fusion

## Slide 4: Why nuclear fusion energy needs trustworthy simulation (continued)
Tokamak confines plasma (temperature around 150 million °C) in a magnetic “cage” long enough to fuse.
Accurate and scalable simulations needed before expensive and time-consuming physical experiments.
Simulations must be trustworthy. Plausible-looking wrong answer is worse than no answer.
Tokamak magnetic confinement (U.S. DOE)

## Slide 5
Schematic of a nuclear fusion power plant.

## Slide 6: The modeling challenge
Turning fusion physics into correct and fast HPC code needs scarce and implicit expertise.
Numerical methods: Choose grids, discretizations, and solvers that actually converge.
Library: Express it in PETSc (Portable, Extensible Toolkit for Scientific Computation) a library for high-performance computing.
Parallelism: Run on many CPU cores / GPUs.
Verification: Prove the computed answer is right, not merely plausible.
Question: can a multi-agent AI system automate this whole path, and can we trust it?

## Slide 7: The problem: Grad–Shafranov equilibrium
Axisymmetric ideal-MHD force balance for the poloidal flux .
Equilibrium magnetohydrodynamics for 2-dimensional plasma in a tokamak:
where is magnetic flux, is plasma pressure, is magnetic permeability, , and are the cylindrical coordinates.
Elliptic, non-linear, time-independent.
Its solution gives the flux surfaces, magnetic axis, and safety factor .
A natural problem for PETSc SNES (Scalable Non-linear Equations Solvers).
Verifiable: a manufactured exact solution gives a rigorous convergence test.
Flux surfaces of the verified solution

## Slide 8: The system: 3-layer multi-agent AI pipeline
PETSc Model-Context-Protocol (MCP) agents, coordinated end to end.
Problem definition (Mathematical Modeling agent) → strong / weak form, name, time-dependence.
Agent execution (Numerical Analysis agent): grid, discretization, solver (SNES).
Agent execution (HPC Code Generation agent): writes, compiles and runs PETSc C programs.
Execution substrate (Compile and Run agent): make / run on the real machine.
All agents run against Argonne’s Argo gateway (Claude Opus 4.8).
A project-owned driver records every artifact with provenance (reproducible and resumable).

## Slide 10: The AI pipeline in action
From one English prompt to a compiled, running solver, with no human edits.
Prompt: “the Grad-Shafranov equilibrium for the plasma in a tokamak.”
Modeling AI agent: identified ‘Grad-Shafranov equation’; time-dependent = False.
Numerical Analysis AI agent: non-linear solve with SNES on a structured grid.
Code Generation AI agent: 267-line PETSc program (DMDA + SNES + true Jacobian).
Compiled and ran on 1 and 4 MPI ranks. No human edits.

## Slide 11: AI-agent-generated PETSc solver (excerpt)
A true-Jacobian finite-difference SNES residual, written by the Code Generation AI agent.
static PetscErrorCode FormFunction(SNES snes, Vec X, Vec F, void *ctx){
/* Delta*_h psi = (psi_E-2psi_C+psi_W)/hR^2
- (1/R)(psi_E-psi_W)/(2hR)
+ (psi_N-2psi_C+psi_S)/hZ^2 */
f[j][i] = dRR - dR1/R + dZZ - ForcingF(user,R,Z); /* residual */
}
SNESSetFunction(snes, r, FormFunction, &user);
SNESSetJacobian(snes, J, J, FormJacobian, &user); /* true Jacobian */
SNESSolve(snes, NULL, x);

## Slide 12: Verification: it is actually right
Method of manufactured solutions: a measured order of accuracy, not just plausible output.
Known exact : check the numerical error as the grid refines.
Max-norm error = on the finest grid.
Observed order of accuracy (expected 2 for central differences).
SNES converged: CONVERGED_FNORM_RELATIVE.
Manufactured-solution convergence

## Slide 13: Decision-gate metrics
Correctness, human effort, and efficiency: the numbers behind the demo.
Correctness:
  model identified,
  C programs compiled and ran,
  second-order convergence.
Human effort: 0 lines of solver code hand-written. It was all AI-generated.
Efficiency: total wall-clock ≈ 450.8 seconds; code-gen used 5 tool calls.
Around 23 completions of LLM (large language models) across the whole pipeline.

## Slide 14: Fully autonomous: the built-in orchestrator
The shipped LLM orchestrator drives all four agents itself (no Python driver).
Given only the prompt, an inner Claude agent sequenced all four MCP servers on its own.
It independently chose a Solov’ev Grad–Shafranov model and a DMPLEX + PetscFE finite-element solve.
The generated code compiled cleanly and ran: 225 DOFs, L2 norm , return code 0.
It surfaced a real upstream bug: a hard-coded iteration cap flagged a converged run as failure.
We fixed it and contributed the patch; the re-run finished: “I have completed the orchestration.”

## Slide 15: What we built and contributed
Reusable tooling around the agents, plus fixes contributed back upstream.
A project-owned orchestration driver with full artifact provenance (resumable).
Verification + post-processing (convergence, flux surfaces) and a metrics harness.
Four fixes contributed back to the open PETSc multi-agent system:
  CWD-independent server resolution; portable stdio interpreter.
  graceful operation without the documentation / RAG services.
  code-generation and orchestrator loops that reliably capture results.

## Slide 16: Takeaways and next steps
A verification-driven multi-agent path from prompt to trustworthy HPC code
A multi-agent AI system generated a correct, verified PETSc fusion-MHD solver from a prompt.
Both the Python driver and the fully-autonomous orchestrator succeeded end to end.
Verification-driven: convergence + exact-solution checks, not just plausible output.
Next: shaped real-machine equilibria (Solov’ev / Cerfon–Freidberg), q-profile, GPU scale-up.
Code + docs: github.com/engineer-scientist/petsc_mcp_servers_tokamak

## Slide 17: References and acknowledgements
AI coding agent: Claude Code by Anthropic (https://claude.com/product/claude-code)
Advisors: Dr Junchao Zhang, Dr Lois Curfman McInnes, Prof Matthew Knepley.
Automated Problem-to-Solution Generation for PDE-Based Simulation Science, Dr Lois Curfman McInnes, Dr Junchao Zhang, Dr Matthew Knepley, et al (2026).
PETSc MCP Servers, Barry Smith (2026): https://gitlab.com/petsc/petsc_mcp_servers
Grad-Shafronov equation (https://en.wikipedia.org/wiki/Grad-Shafranov_equation).
ANL CELS General Computing Environment: https://help.cels.anl.gov/docs/linux/